## Slide 1
WebRTC in a
Radio-Controlled Car via 5G
Raul Hidalgo Caballero
Master in Computer Engineering
Director: David Sarrat González
University of Lleida, September 2026
Notes: Timing: 30 seconds
Introduce the project as a video-path study built around a physical RC-car prototype.
State the central design choice: the application server coordinates peers but does not carry video.
Sources:
- TFM.docx, cover and pp. 7–9.
- UdL brand: https://www.imatge.udl.cat/ca/marca/color-corporatiu/

## Slide 2
OPENING
Research Question
02
Can an RC car deliver live video to a remote browser with less than 400ms glass-to-glass latency?
< 400 ms
LATENCY TARGET
5G
Intended deployment context
4G
Prototype validation actually performed
The presentation keeps the target and the evidence separate.
Notes: Timing: 50 seconds
Read the question once, then separate the intended 5G context from the network used for the prototype measurement.
Do not imply that the thesis validated 5G behavior. The tested mobile link used a Huawei 4G dongle.
Sources:
- TFM.docx, pp. 7–9, 13, 36–37.

## Slide 3
OPENING
Project Scope
03
“
The project scope is to establish a low-latency video connection between an RC car and a remote web browser, targeting a glass-to-glass latency below 400 ms. Data transport and vehicle control are not included.
VIDEO INCLUDED
Capture, encode, negotiate, transport, play
DATA / CONTROL EXCLUDED
No command loop, actuation, or safety controller
Notes: Timing: 55 seconds
Use the exact scope statement because later slides discuss control only as future work.
The repository contains unused DataChannel scaffolding, but it does not implement vehicle control.
Sources:
- PLAN.md, Project Scope.
- TFM.docx, pp. 8–9 and 37.
- Repository: useRtcPeerConnection.tsx and WebRtcSessionManager.cs; DataChannels are created but unused.

## Slide 4
OPENING
Presentation Roadmap
04
01
Theory
9 min
02
Issues and Iterations
10 min
03
Future Work
3 min
04
Potential Applications
2 min
05
Demo / Video
3 min
Notes: Timing: 45 seconds
Preview the five main sections in this exact order.
The timings leave about one minute for transitions inside the thirty-minute defense.
Sources:
- PLAN.md, Slide Structure and Visual and Source Treatment.

## Slide 5
THEORY
WebRTC as a Whole
05
RTCPeerConnection
Browser and native APIs
Application-defined signaling
ICE connectivity
DTLS-SRTP encryption
Real-time media
Congestion control
WebRTC combines APIs and protocols. It does not prescribe how the application carries signaling messages.
Notes: Timing: 60 seconds
Present WebRTC as a system rather than a single wire protocol.
The browser API manages peer state. The IETF protocols provide connectivity, secure media transport, and feedback.
SignalR is an application choice for signaling because WebRTC deliberately leaves that transport open.
Sources:
- RFC 8825: https://www.rfc-editor.org/rfc/rfc8825.html
- W3C WebRTC: https://www.w3.org/TR/webrtc/
- RFC 9429 JSEP: https://www.rfc-editor.org/rfc/rfc9429.html
- TFM.docx, p. 20.

## Slide 6
THEORY
The WebRTC Protocol Stack
06
Notes: Timing: 60 seconds
Walk from capture at the top to UDP and IP at the bottom.
RTP and RTCP carry media and feedback. WebRTC protects them as SRTP and SRTCP.
DTLS-SRTP derives media keys on the selected ICE path. DataChannel is part of the standard but outside this project's implemented scope.
Sources:
- RFC 8835: https://www.rfc-editor.org/rfc/rfc8835.html
- RFC 8834: https://www.rfc-editor.org/rfc/rfc8834.html
- RFC 3711: https://www.rfc-editor.org/rfc/rfc3711.html
- RFC 5764: https://www.rfc-editor.org/rfc/rfc5764.html
- TFM.docx, pp. 22–23.

## Slide 7
THEORY
STUN and TURN
07
STUN: discover and test a direct path
Peer A
private address
STUN
public mapping
Peer B
private address
MEDIA DIRECT WHEN REACHABLE
TURN: relay when direct checks fail
Peer A
TURN relay
public allocation
Peer B
MEDIA USES RELAY
PATH
Direct preferred
Extra relay hop
LATENCY
Usually lower
May increase
BANDWIDTH
Endpoint traffic
Relay carries all media
INFRASTRUCTURE
STUN is lightweight
TURN capacity costs
Notes: Timing: 70 seconds
STUN reveals a public-facing mapping and supports connectivity checks. It does not relay the video.
TURN provides a reachable public relay allocation when direct checks fail.
ICE generally prefers direct candidates. The relay improves reliability but consumes relay bandwidth and may add latency because media takes an extra hop.
Sources:
- RFC 8489 STUN: https://www.rfc-editor.org/rfc/rfc8489.html
- RFC 8656 TURN: https://www.rfc-editor.org/rfc/rfc8656.html
- RFC 8445 ICE: https://www.rfc-editor.org/rfc/rfc8445.html
- TFM.docx, pp. 21–22.

## Slide 8
THEORY
SDP Offer and Answer
08
Raspberry Pi
OFFERER
SignalR server
FORWARDS ONLY
Remote browser
ANSWERER
SDP OFFER VIA SIGNALR
SDP ANSWER VIA SIGNALR
01
media sections and direction
02
codecs and RTP parameters
03
ICE credentials
04
DTLS fingerprints
SignalR transports the descriptions. It does not interpret or terminate the media session.
Notes: Timing: 65 seconds
The Raspberry Pi creates the offer after a browser joins. SignalR forwards that offer to the selected browser.
The browser applies the offer, creates the answer, and returns it through the hub.
SDP carries the parameters needed to agree on media and establish ICE and DTLS. The application server does not become a media endpoint.
Sources:
- RFC 8866 SDP: https://www.rfc-editor.org/rfc/rfc8866.html
- RFC 9429 JSEP: https://www.rfc-editor.org/rfc/rfc9429.html
- TFM.docx, pp. 21, 33–34.
- Repository: WebRtcSessionManager.cs, WebRtcSignalingBackgroundService.cs, Control.tsx.

## Slide 9
THEORY
ICE Candidates After SDP
09
1
Initial SDP
offer / answer
2
Candidates
trickle
3
Connectivity
checks
4
Pairs ranked
by priority
5
Winning pair
nominated
HOST
local interface
SRFLX
mapping learned via STUN
PRFLX
mapping learned in checks
RELAY
TURN allocation
Gathering and SDP creation can overlap at runtime. Trickle ICE sends candidates as soon as they appear.
Notes: Timing: 70 seconds
Present SDP first for explanatory clarity, then note that gathering can already be in progress while the descriptions are created.
Trickle ICE sends candidates incrementally. Each side forms pairs, runs STUN checks, ranks viable paths, and nominates the selected pair.
Peer-reflexive candidates can appear during checks even when they were not gathered beforehand.
Sources:
- RFC 8445: https://www.rfc-editor.org/rfc/rfc8445.html
- RFC 8838: https://www.rfc-editor.org/rfc/rfc8838.html
- W3C ICE events: https://www.w3.org/TR/webrtc/#rtcpeerconnectioniceevent
- TFM.docx, p. 21.

## Slide 10
THEORY
WebRTC Video Encodings
10
VP8
Mandatory to implement
H.264 Constrained Baseline
Mandatory to implement
VP9 / AV1
Optional modern choices
H.265
Fragmented support; no universal browser assumption
CURRENT PROJECT PIPELINE
Camera
MJPEG
FFmpeg
decode + encode
H.264
Baseline
Negotiation, not a fixed assumption
Mandatory-to-implement means an interoperability baseline.
The selected codec still depends on offer/answer negotiation.
The project advertises H.264 packetization-mode=1 with profile-level-id 42e01f.
Notes: Timing: 65 seconds
VP8 and H.264 Constrained Baseline form the mandatory video interoperability baseline for WebRTC endpoints that support video.
VP9 and AV1 depend on endpoint capabilities. H.265 cannot serve as a universal browser assumption.
The prototype converts the C920 MJPEG stream to H.264. Its SDP advertises packetization mode 1 and profile-level-id 42e01f.
Sources:
- RFC 7742 sections 5–6: https://www.rfc-editor.org/rfc/rfc7742.html#section-5
- W3C getCapabilities: https://www.w3.org/TR/webrtc/#dom-rtcrtpsender-getcapabilities
- TFM.docx, pp. 23–24.
- Repository: CameraVideoSource.cs lines 28–35 and appsettings.json.

## Slide 11
THEORY
WHIP and WHEP
11
Publisher / device
Central media server
Viewer / browser
WHIP
ingest
WHEP
egress
WebRTC session 1
WebRTC session 2
HTTP session lifecycle
POST offer, 201 answer + Location, PATCH ICE updates, DELETE teardown
WHIP is RFC 9725. WHEP remains draft-ietf-wish-whep-04 as of 5 September 2026.
Notes: Timing: 70 seconds
WHIP covers unidirectional ingest from a publisher to a media server. WHEP covers egress from a media server to a viewer.
Combining them normally creates two server-terminated WebRTC sessions, so the media server sits in the video path.
WHIP is a Standards Track RFC. WHEP is still an active Internet-Draft, revision 04, on the date of this defense.
Sources:
- RFC 9725: https://www.rfc-editor.org/rfc/rfc9725.html
- WHEP draft-04: https://www.ietf.org/archive/id/draft-ietf-wish-whep-04.html
- WHEP status: https://datatracker.ietf.org/doc/draft-ietf-wish-whep/
- TFM.docx, pp. 24–25.

## Slide 12
THEORY
WHIP/WHEP Concepts Implemented Through SignalR
12
“I implemented the WHIP and WHEP signaling concepts through SignalR. I did not implement the complete HTTP protocols because WHIP and WHEP are designed for device-to-central-server ingestion and central-server-to-browser egress. This project keeps the central server outside the video path and uses it only for signaling.”
CONCEPT MAPPING
Publisher / viewer
device / browser
SDP exchange
SignalR offer / answer
ICE updates
SignalR candidate events
Session lifecycle
hub group + peer state
Termination
partial disconnect / cleanup
Protocol status
HTTP endpoints return 501
Concepts mapped. Protocol compliance remains unimplemented.
Notes: Timing: 80 seconds
Read the statement directly because it resolves a central architectural distinction.
The project maps publisher and viewer roles, SDP and ICE exchange, and peer state through SignalR. Termination is only a partial disconnect and cleanup mapping, not a complete protocol lifecycle.
The current WHIP and WHEP controller methods contain TODOs and return HTTP 501. They provide neither the required session resources nor the PATCH and DELETE lifecycle.
Sources:
- PLAN.md, required statement.
- RFC 9725: https://www.rfc-editor.org/rfc/rfc9725.html
- WHEP draft-04: https://www.ietf.org/archive/id/draft-ietf-wish-whep-04.html
- Repository: DevicesController.WhipAsync.cs and DevicesController.WhepAsync.cs.

## Slide 13
ISSUES AND ITERATIONS
Initial Prototype Architecture
13
RC car / Raspberry Pi
Camera + WebRTC sender
ASP.NET Core
SignalR coordination
Remote browser
React + WebRTC viewer
STUN
public mapping + checks
SIGNALING
SIGNALING
EXPECTED DIRECT WEBRTC VIDEO
Initial assumption: STUN would expose a usable route. TURN was not yet part of the architecture.
Notes: Timing: 50 seconds
The first design already separated signaling from media. ASP.NET and SignalR coordinated the two peers, while WebRTC was expected to carry video directly.
The early configuration contained Google STUN only. TURN was explicitly absent.
Sources:
- Repository history: commit 5b2433a, 14 February 2026; commit 6bc9041, 19 February 2026.
- TFM.docx, pp. 16–19.

## Slide 14
ISSUES AND ITERATIONS
The NAT Problem
14
Raspberry Pi
192.168.x.x
Mobile hotspot
private IPv4
Carrier-grade NAT
shared public IPv4
Browser NAT / firewall
Browser
private IPv4
STUN discovers a mapping
Mapping discovered ≠ inbound path guaranteed
WHY DIRECT CHECKS CAN FAIL
Destination-dependent mappings
Blocked inbound UDP
Multiple translation layers
Notes: Timing: 60 seconds
Both endpoints can sit behind private IPv4 addressing. The mobile side adds carrier-grade NAT, and the browser side may add another NAT and firewall.
STUN can reveal a mapping without proving that the remote peer can send to it. Destination-dependent mapping and blocked inbound UDP can still defeat direct checks.
Sources:
- RFC 8489: https://www.rfc-editor.org/rfc/rfc8489.html
- RFC 8445: https://www.rfc-editor.org/rfc/rfc8445.html
- TFM.docx, pp. 21–22 and 36–38.

## Slide 15
ISSUES AND ITERATIONS
Discovery of TURN
15
14 FEB
STUN only
Direct path expected
01 MAR
TURN added
Relay fallback joins ICE
Device
Browser
TURN relay
DIRECT CANDIDATES PREFERRED
RELAY FALLBACK WHEN DIRECT CHECKS FAIL
Reliability improves; the relay adds infrastructure and carries every media byte.
Notes: Timing: 55 seconds
STUN did not work across every network. TURN therefore became an ICE fallback rather than the preferred path.
The application server still stays outside the video path. When ICE selects a relay candidate, the separate TURN server carries the encrypted media.
Sources:
- Repository history: commit 5b2433a and commit 66702f6 / merge adeac59.
- RFC 8656: https://www.rfc-editor.org/rfc/rfc8656.html
- TFM.docx, pp. 16–19, 21–22.

## Slide 16
ISSUES AND ITERATIONS
Discovery of IPv6
16
PROMISING
ICE can test IPv6 beside IPv4 and TURN.
NOT YET VALIDATED
Only local IPv6 loopback exists in code; WAN behavior remains untested.
Mobile device
Remote browser
IPv4
carrier-grade NAT
IPv4 NAT / firewall
IPv4 path
IPv6 Internet
Firewall policy
IPv6 can avoid the IPv4 CGNAT layer, but not firewall policy or latency limits.
Notes: Timing: 50 seconds
IPv6 could remove the mobile carrier-grade IPv4 translation layer, so ICE should test it alongside IPv4 and TURN.
IPv6 does not bypass endpoint firewalls and is not automatically faster.
The current repository uses IPv6 loopback only between FFmpeg and .NET. No end-to-end public IPv6 test has been recorded.
Sources:
- TFM.docx, pp. 36 and 38.
- Repository: CameraVideoSource.cs line 158 uses IPv6Loopback for local RTP only.
- RFC 8445: https://www.rfc-editor.org/rfc/rfc8445.html

## Slide 17
ISSUES AND ITERATIONS
Discovery of WHIP and WHEP
17
Specifications clarified
publisher and viewer roles
SDP and ICE exchange
session creation and teardown
Architecture decision
Full HTTP WHIP / WHEP
Central media server
terminates both sessions
Rejected for this architecture
SignalR concept mapping
Application server stays
outside the video path
Adopted
HTTP endpoints remain stubs
POST validates SDP, then returns HTTP 501
Notes: Timing: 50 seconds
WHIP and WHEP supplied a useful vocabulary for publisher, viewer, signaling state, and teardown.
A complete implementation would put a central media server into the video path, which conflicts with this project's central architectural goal.
The concepts moved into the SignalR flow. The HTTP actions remain explicit stubs.
Sources:
- RFC 9725: https://www.rfc-editor.org/rfc/rfc9725.html
- WHEP draft-04: https://www.ietf.org/archive/id/draft-ietf-wish-whep-04.html
- Repository history: commits 248f094, 529de9a, 72b7dd1, 87bc7cc.

## Slide 18
ISSUES AND ITERATIONS
Camera Integration Iterations
18
Approach | Repository status | Strength | Limitation / trade-off
libcamera | Considered | Native Raspberry Pi camera stack for CSI cameras | No recorded implementation. Final Logitech C920 capture uses V4L2.
FFmpeg shared libraries | Implemented first | Direct in-process encoded-sample callbacks | Required exact FFmpeg 8.1 native-library and FFmpeg.AutoGen compatibility.
External FFmpeg RTP emission | Final implementation | Executable supervision creates a clearer deployment boundary | Adds loopback RTP depacketization and WebRTC repacketization.
External FFmpeg solved native-library fragility, not software encoding load.
Notes: Timing: 70 seconds
libcamera was considered as the Raspberry Pi CSI-camera stack, but no recorded revision implemented it. The final USB-camera path uses V4L2.
The first implementation used SIPSorceryMedia.FFmpeg and FFmpeg.AutoGen for direct callbacks, which coupled deployment to exact native FFmpeg libraries.
The final version supervises an FFmpeg executable and receives H.264 over loopback RTP. That boundary is easier to deploy but adds depacketization and repacketization.
Sources:
- Repository history: commit 4b357dd, historical PLAN at 3f9931d, and commit d8e2a27.
- TFM.docx, pp. 29–30 and 36.

## Slide 19
ISSUES AND ITERATIONS
Final Media Pipeline
19
FFMPEG PROCESS
.NET + SIPSORCERY
Logitech C920
MJPEG
V4L2
capture
MJPEG
decode
libx264
H.264 baseline
RTP over
IPv6 loopback
RTP parse +
H.264 depacketize
Annex-B +
SPS / PPS
SIPSorcery
WebRTC / SRTP
Browser
playback
1280×720 at 30 fps, 1.5 Mb/s, superfast, zerolatency, no B-frames
FFmpeg captures and encodes; SIPSorcery owns the secure WebRTC peer connection.
Notes: Timing: 80 seconds
Follow the pipeline from the C920 to the browser. FFmpeg receives MJPEG through V4L2, decodes it, and software-encodes H.264 Constrained Baseline.
FFmpeg emits RTP on IPv6 loopback. .NET parses RTP, depacketizes H.264, assembles Annex-B access units, and caches SPS and PPS.
SIPSorcery repacketizes the encoded access unit into the negotiated WebRTC stream and owns SRTP and the peer connection.
The .NET layer avoids a second decode and encode, but FFmpeg still performs the MJPEG decode and software H.264 encode.
Sources:
- TFM.docx, pp. 29–30 and 36.
- Repository: appsettings.json; CameraVideoSource.cs lines 152–188, 359–493; WebRtcSessionManager.cs lines 99–101 and 247–264.

## Slide 20
ISSUES AND ITERATIONS
Discovery of CPU Encoding Cost
20
WORK ON THE RASPBERRY PI
1
Decode camera MJPEG
CPU + memory bandwidth
2
Software-encode H.264
CPU + heat + latency
3
Packetize and encrypt
Additional real-time work
LOW-LATENCY SETTINGS
superfast zerolatency no B-frames small VBV buffer
External FFmpeg improved deployment isolation; CPU encoding stayed on the Pi.
Notes: Timing: 60 seconds
The camera outputs MJPEG, so FFmpeg must decode every frame before libx264 can encode H.264 in software.
Discuss CPU, memory bandwidth, heat, and latency qualitatively. No measured CPU percentage exists in the evidence.
The external process made deployment more robust. It did not remove the compute cost.
Sources:
- TFM.docx, pp. 29–30 and 36–39.
- Repository: appsettings.json and CameraVideoSource.cs.
- Image: TFM.docx Figure 3, Raspberry Pi 5 product image.

## Slide 21
ISSUES AND ITERATIONS
Electrical Input to the Raspberry Pi
21
AUTHOR-REPORTED OBSERVATION
Motor demands
high current
Supply voltage
dips
Raspberry Pi
disconnects briefly
NiMH supply
PROTECTED POWER DESIGN
Separate fused branch
DC-DC regulation + decoupling
Transient suppression + grounding
Add brownout monitoring and verify worst-case motor-stall current before field tests.
Notes: Timing: 50 seconds
When the car demands too much current, the Raspberry Pi disconnects momentarily. Treat this as an author-reported observation because the thesis does not document a measured incident trace.
The thesis does support the mechanism and mitigation: motor-stall peaks, supply monitoring, a fused branch, transient protection, decoupling, and careful grounding.
Sources:
- PLAN.md, Issues with electrical input to the RPI.
- TFM.docx, pp. 13 and 39.
- Image: TFM.docx Figure 6, NiMH battery.

## Slide 22
ISSUES AND ITERATIONS
Prototype Result and Limitations
22
340 ms
ONE OBSERVATION
Glass-to-glass under the tested 4G configuration
TARGET
< 400 ms
1788024617068 − 1788024616728 = 340 ms
Evidence of feasibility, not a statistical guarantee or completed 5G validation
Notes: Timing: 75 seconds
The measurement compares the visible time reference with the received browser image. The two Unix timestamps differ by exactly 340 milliseconds.
The browser status line shows a relay local candidate in this captured run, so the observed path appears TURN-relayed.
Treat this as one 4G observation that supports feasibility. It does not establish a latency distribution, a guarantee, or 5G validation.
Sources:
- TFM.docx, pp. 8–9 and 36; Figure 10.
- Resum-TFG-TFM-Raul-Hidalgo-Caballero.docx.pdf, p. 2.

## Slide 23
FUTURE WORK
Complete Remote Control
23
NEXT PHASE
Add a verified command loop without changing the completed video-scope claim.
INPUT
periodic gamepad sampling
MESSAGE
version + sequence + timestamp
DEVICE
range and staleness checks
ACTUATION
steering and throttle PWM
Fail safe to neutral on timeout, invalid data, channel loss, or emergency stop.
Notes: Timing: 45 seconds
Vehicle control belongs to the next phase, not the completed project scope.
A production command loop needs explicit sequencing, timestamps, validation, actuation, and a neutral fail-safe whenever communication or input becomes unsafe.
Sources:
- TFM.docx, pp. 37–38.
- Image: TFM.docx Figure 2, 3D chassis design.

## Slide 24
FUTURE WORK
Hardware and Direct H.264
24
CURRENT
C920
MJPEG
MJPEG
decode
Software
libx264
TARGET
Camera or SoC
H.264 output
Packet adaptation
only
Remove two expensive stages where hardware permits
Validate profile, SPS/PPS, GOP, bitrate, buffering, CPU load, and measured latency.
Notes: Timing: 35 seconds
The best next optimization is direct H.264 from the camera or a hardware encoder, removing MJPEG decode and software libx264 where possible.
Direct output still needs validation. The profile, parameter sets, packetization, GOP, buffering, and measured latency must match the WebRTC path.
Sources:
- TFM.docx, pp. 38–39.
- Image: TFM.docx Figure 4, Logitech HD Pro C920.

## Slide 25
FUTURE WORK
Network Resilience
25
PLANNED TEST MATRIX
Candidate path | 4G | 5G NSA | 5G SA
IPv4 direct | Planned | Planned | Planned
IPv6 direct | Planned | Planned | Planned
TURN relay | Planned | Planned | Planned
RECORD FOR EVERY RUN
connection success
latency distribution
jitter + loss
mobility stability
uplink consistency
Notes: Timing: 35 seconds
Run a controlled matrix rather than another single demonstration. Compare IPv4 direct, IPv6 direct, and TURN relay across realistic mobile network modes.
Record distributions and stability, not only a best-case latency number. Include NAT type, mobility, loss, and uplink consistency.
Sources:
- TFM.docx, pp. 38 and 40.
- RFC 8445: https://www.rfc-editor.org/rfc/rfc8445.html

## Slide 26
FUTURE WORK
Protected Electrical Design
26
HARDWARE TRACK
Battery
Fuse + transient
protection
Dedicated DC-DC
regulator
Raspberry Pi
Motor branch
Separate noisy motor current from the compute rail; add decoupling, strain relief, and brownout logging.
SEPARATE PROTOCOL TRACK
Complete WHIP / WHEP
Implement session resources, Location, PATCH, DELETE, HTTPS, and authorization if a central media-server architecture becomes a requirement.
This protocol track changes the media architecture and must be evaluated explicitly.
Notes: Timing: 35 seconds
The hardware priority is a protected and measurable power tree that isolates motor transients from the Raspberry Pi rail.
The plan also calls for complete WHIP and WHEP. That is a separate protocol track because true compliance requires HTTP session resources and a central media server that terminates WebRTC.
Sources:
- TFM.docx, p. 39.
- RFC 9725: https://www.rfc-editor.org/rfc/rfc9725.html
- WHEP draft-04: https://www.ietf.org/archive/id/draft-ietf-wish-whep-04.html

## Slide 27
FUTURE WORK
ESP32-P4 Integrated Rust Platform
27
CANDIDATE PLATFORM, NOT IMPLEMENTED
MIPI-CSI
camera
ISP +
H.264 encoder
Rust application
media + safety state
Ethernet or
external radio / modem
WHY INVESTIGATE
Dual-core RISC-V
Camera + ISP
Hardware H.264
Ethernet MAC
OPEN QUESTIONS
WebRTC stack and memory budget
Rust driver maturity
Thermal and power envelope
5G modem integration
Espressif documents H.264 encode up to 1080p30. End-to-end feasibility still requires a prototype.
Notes: Timing: 30 seconds
ESP32-P4 is a long-term consolidation candidate because it combines RISC-V cores, camera interfaces, an image pipeline, hardware H.264, and Ethernet.
It has no integrated 5G radio, so a modem or network companion remains necessary. Rust HAL support exists, but peripheral maturity and a practical WebRTC stack still need validation.
Sources:
- TFM.docx, p. 39.
- Espressif ESP32-P4 datasheet: https://documentation.espressif.com/esp32-p4_datasheet_en.html
- Espressif product overview: https://www.espressif.com/en/node/7617
- esp-hal: https://github.com/esp-rs/esp-hal

## Slide 28
POTENTIAL APPLICATIONS
Autonomous Motorway Driving with Remote Final Approach
A truck handles the long motorway segment autonomously. A remote driver takes over for depot entry, loading areas, and other complex final manoeuvres.
This project contributes the low-latency video path. Safe teleoperation also requires redundant control, vehicle safety systems, and operational approval.
CONCEPT ILLUSTRATION
Notes: Timing: 60 seconds
Use this as an application concept, not as a tested system.
The motorway segment can run autonomously, while a remote operator handles the final approach where context and interaction are harder to automate.
Low-latency video is one dependency. Production teleoperation needs redundant control, a safety case, secure operations, and regulatory approval.
Sources:
- Application example specified in PLAN.md.
- Concept illustration generated for this presentation with OpenAI ImageGen; it is not project evidence.

## Slide 29
POTENTIAL APPLICATIONS
Teleoperated Heavy Vehicles
CRANES
Move operators away from suspended loads
MINING
Operate in dust, heat, and unstable terrain
WORKBOATS
Support manoeuvres in hazardous port areas
Concept only. Production systems require redundant command paths and task-specific safety engineering.
Notes: Timing: 60 seconds
Cranes, mining equipment, and workboats share the value proposition of moving people away from hazardous work zones.
The video link must remain usable under motion, vibration, coverage changes, and harsh radio conditions.
The prototype addresses only the video-path question. Each domain needs its own redundant control and safety design.
Sources:
- Application examples specified in PLAN.md.
- Concept illustration generated for this presentation with OpenAI ImageGen; it is not project evidence.

## Slide 30
DEMO / VIDEO
Demo Setup
30
TWO INPUT PATHS
Physical car
Raspberry Pi + C920 + mobile link
Browser simulator
Countdown video captured as a WebRTC track
Audience checklist: SignalR, SDP offer/answer, ICE candidate type, connection state, live video
The selector lists prototype entries; it is not a production fleet registry.
Notes: Timing: 40 seconds
Show the physical device path first when available. Keep the browser simulator ready as the technical fallback.
Ask the audience to watch signaling state, the offer and answer, candidate types, connection state, and the video itself.
The device selector uses hard-coded prototype entries and should not be described as live fleet discovery.
Sources:
- TFM.docx, p. 32; Figure 9.
- Repository: Index.tsx, Control.tsx, ControlTest.tsx.

## Slide 31
DEMO / VIDEO
Live Demo Sequence
31
1
Start server
Open the selector page
2
Start device
Use the car or simulator
3
Open viewer
Viewer join triggers the offer
4
Exchange SDP + ICE
SignalR carries both
5
Inspect selected path
host, srflx, or relay
6
Show live video
Demonstrate the latency target
Demo ordering detail
The real device creates an offer when it receives ClientJoined. Start it before opening or reloading the viewer page.
Notes: Timing: 45 seconds
Start the central server and selector page. Then connect the device or start the simulator before opening the viewer route.
The viewer join event triggers the device offer. SignalR transports the SDP and Trickle ICE candidates.
Show the candidate types and connected state, then the live video and latency demonstration.
Do not demonstrate vehicle control as completed project scope.
Sources:
- Repository: WebRtcSignalingBackgroundService.cs lines 25–32; WebRtcHub.cs; Control.tsx.
- PLAN.md, Live Demo Sequence.

## Slide 32
DEMO / VIDEO
Fallback Video
32
PHYSICAL-CAR RECORDING PLACEHOLDER
Replace with a 45–60 second RC-car demonstration before the defense
SIMULATOR ASSET
The committed countdown video supports a technical fallback only. It is not physical-car evidence.
Notes: Timing: 55 seconds
This slide reserves the required 16:9 media frame for a real RC-car recording.
No physical-car video file exists in the repository. The countdown is a 66.94-second simulator asset and can demonstrate the signaling and media path only.
Keep the placeholder label until real footage is inserted.
Sources:
- Repository: src/ScarletRadioControl.Web.Frontend/src/assets/countdown.mp4 and ControlTest.tsx.
- PLAN.md, Fallback Video.

## Slide 33
FINAL TAKEAWAYS
WebRTC can meet the prototype latency target
One 4G run measured approximately 340 ms glass-to-glass.
NAT traversal and software encoding drove the main engineering iterations.
Hardware H.264, broader network testing, and production relay capacity are the next priorities.
Questions?
Physical prototype stream
Notes: Timing: 40 seconds plus questions
Close with the evidence: the prototype demonstrates feasibility under one tested 4G configuration.
The most consequential engineering work involved NAT traversal and the software media pipeline.
Name the next priorities, then invite questions.
Sources:
- TFM.docx, pp. 36–40; Figure 11.
- PLAN.md, Final Takeaways and Questions.